## Slide 1: State of protocol compression in IoT
Rahul Jadhav
Pre-IETF100 2017, Bangalore
Notes: Can really IPv6 be used for last-mile IoT networks? Isn’t it a lot of overhead just to get IP in the last mile? Are we compromising on the last mile goodput just to fit in IPv6?
IPv6 compression is one key thing which has allowed use of IP in the last-mile and thus making end-to-end IP connectivity possible.

## Slide 2: Compression Scenarios – pre-IoT era
Low-or-medium speed links such as satellite and cellular
VoIP calls
  20ms audio data is ~20 octets (G.729 codec) and control overhead (RTP/UDP/IPv4) is 40 octets
Gaming applications: Small and latency critical payload
Tunneling overhead (IPv6/IPv6/TCP header = 100 octets)
Notes: Goodput improves when you reduce header overhead.
Header compression is about link efficiency…
Support for higher node densities..

## Slide 3: Protocols Compression
Header Compression Fundamentals
  Usually per-link compression
  Temporal Compression:
    Redundancy between consecutive packets of the same flow
  Robustness:
    Impact of packet-loss and reordering on packet reconstruction
  Increased robustness comes at an expense of lower compression efficiency
Payload Compression

## Slide 4
1990
1999
2001
2003
2008
CTCP / VJ Compression
Delta Encoding for TCP/IP compression
ROHC
ROHCv2
Simplified
More robust
More profiles
IPHC, CRTP
Arbitrary IP, TCP, UDP header compression
No use of delta encoding for non-tcp packets
eCRTP
Per-flow compression context
Closed-Loop – thus feedback
Compression efficiency inversely proportional to packet loss, reordering
Robust (than IPHC)
Quick context resynchronization
Robust (than CRTP)
Quick context resynchronization

## Slide 5: IoT conditions
Constraints everywhere…
  Network & Device constraints
  Thousands of devices may connect to a single gateway
Some characteristics to work with…
  Only couple or more of flows per device
  Limited traffic flow per device
Compression allows
  Reduction of packet fragmentation
  Improvement in good-put of last-mile constrained network
Notes: Device Resource Constraints:
- Limited memory, thus cannot have complex compression algorithms implemented.

## Slide 6
Are IPHC/ROHC/… good candidates for such conditions?
Per-flow context – An overkill for IoT
Requirement of compression at multiple hops
Cannot afford closed-loop systems
Designed for high throughput systems
Notes: Per-flow context is too resource intensive
Compression at multiple hops
Cannot afford closed-loop systems which involves feedback
Designed for higher traffic

## Slide 7: 6LoWPAN Compression (RFC 6282)
Basis for header compression on 802.15.4
  127 Bytes MTU (in 2.4GHz)
  MAC(w/sec) + IPv6 + UDP = 46 + 40 + 8 = 94 Bytes
  Multihop network
Compression
  IPv6 header
  Transport header
  Fragmentation & Reassembly

## Slide 8: 6LoWPAN compression assumptions
Reuse MAC layer information…
  For checksum calculation, payload length derivation
  For address generation
For IPv6 compression
  Use of Stateless Address Auto-configuration (SLAAC)
    Derivation of IPv6 address from MAC ID
  Assumptions of default traffic class & flow, hop limit and other defaults
    But still allows non-default values to be carried uncompressed inline if need be…
  Better UDP hdr compression, if port-range is in (0xf0b0 – 0xf0bf)
6LoRH compression
  IPv6 artefacts (SRH, RPI) compression

## Slide 9: An example…
B
A
IP=fe80::1234
MAC IID=1234
IP=fe80::6543
MAC IID=6543
IP pkt
Src port = 0xf0b2
Dst port = 0xf0ba
CID = Context ID
SAC = Source address compression
DAC = Destination address compression

## Slide 10: Difference to Pre-IoT era header compression
Stateless compression
  No state/context on per-flow basis
  Shared context contains network prefix common to all flows
Packets can be decompressed individually
  without referring to previous packets in the same flow.
  Different packets may take different routes
  Context is light-weight and easy to share (since context is not on per-flow basis)

## Slide 11: Emergence of 6lo-over-foo…
Other candidate link layer technologies …
  BTLE
    Bluetooth Low Energy
  PLC
    Power Line Comm
  NFC
    Near Field Comm
  MS/TP
    Master Slave/Token Passing for RS-485 phy
  DECT-ULE
    Digital Enhanced Cordless Telecomms – Ultra Low Energy
Addressing (SLAAC)
MTU impact on FAR
Neighbor discovery

## Slide 12: Application Protocols Redesign
Use of CoAP (RFC 7252) in place of HTTP
CBOR (RFC 7049) for payload representation in binary format
Use of YANG SIDs (Schema Item iDentifier)
  NETCONF & RESTCONF use string identifiers
  YANG SIDs substitute these string identifiers with unique 64bit uint.
Redesign helps reduce memory footprint as well as reduce network bandwidth usage

## Slide 13: Where are we heading… LPWANs
LPWANs
  Fractional bits per second network
  Long range & star topology
  Small MTU
  Work-in-progress on IETF
RF Tech | Range | Throughput | MTU (B)
LoRa | 2-5 km urban <15km suburban | 0.3 to 50kbps | 256
SIGFOX | 10km urban 50km rural | Up: 100/600 bps Down: 600bps | Up: 12 Down: 8
802.15.4K-2013 (LECIM) | < 20km LoS < 5 km NoLoS | 1.5 bps to 128 kbps | 16/24/32
802.15.4g SUN | 2-3 km LoS | 4.8 to 800 kbps | 2047
Is 6LoWPAN compression good enough?

## Slide 14: SCHC … a new compression scheme
Static Context Header Compression
  Pronounced SCHiC
  Currently a work-in-progress…
Optimized for
  Star Topology
  Predictable traffic pattern
Objective
  Compress upto 0 bytes for well-known headers
Static Context stored on LPWAN device/thing and SCHC gateway

## Slide 15: An example…
Function | Target Value | Matching Operator | Comp/Decomp Factor
F1 | 0x00 | Ignore | Not-sent
F2 | 0x1230 | MSB(12) | LSB(4)
F3 | 0xABC0 | MSB(12) | LSB(4)
[0x00, 0x2812, 0xE3A1]
DROPPED
[0x00, 0x1234, 0xABCD]
RULE: 5
RULE 5 : 0x4D
[0x00, 0x1234, 0xABCD]
Compressor
De-compressor
Notes: https://www.ietf.org/proceedings/97/slides/slides-97-lpwan-45-ipv6udp-static-context-header-compression-coap-schc-00.pdf

## Slide 16: A generic payload compression approach…
Generic header compression (RFC 7400)
LZ77-style compression for IP payload
Decompressor can be very light-weight implementation
But the compressor implementation could be non-trivial
  A trivial implementation may not be able to achieve good compression ratio
  Thus implications on constrained device use
  Certain deployments where devices are not necessarily “extremely” constrained could benefit from such schemes.

## Slide 17: Several challenges remain…
Especially with security solutions…
  Especially with authentication & key management solutions
  Certificate based authentication is challenging with IoT constraints
  Most of the work is work-in-progress…
DICE working group
  DTLS profiles which allow
  Profiling DTLS for specific use-cases thus eliminating generic handshake

## Slide 18
Thank You